## Slide 1: Comparative Study of Power Generation Methods for Mars Mission: Potential of Space Solar Power (SSP) System
Zeyu Zhang, Vinay Simlot, Sean Rankin
May 26, 2017
Present at International Space Development Conference (ISDC 2017)
Allied Universities Team:
Undergraduate students: Miles Johnson, Amy Li, Sean Rankin, Yohnei Shambourger, Vinay Simlot
Graduate students: Clark Esty, Reid Hyland, Joshua Rogers, Alex Walts, Zeyu Zhang
Faculty advisor: Paul Jaffe

## Slide 2: Presentation Outline
Mars Mission Milestones
Surface Power Strategies: Surface Solar vs. Fission-Powered
Martian Space Solar Power (SSP) System Architecture
Wireless Power Transmission (WPT)
Proposed System Characteristics
Conclusions

## Slide 3: Mars Mission Milestones
1910
1948
First Mars Mission draft
Movie “A Trip To Mars”
1970s
Mars 2 and 3
1976
Viking 1 and 2
1997
“Sojourner”
2004
“Spirit” and ”Opportunity”
2011
“Curiosity”
Notes: Project Mars: 35kW w/ steam boiler
Viking 1/2 : 4 solar panels, and radioisotope thermoelectric generators (620 W)
Sojourner – 200 PV cells, 16W of power at noon
Spirit and Opportunity: <1kWh per day with solar
Curiosity – nuclear thermoelectric generator with 110 W steady power

## Slide 4: Mars Environment
Parameter | Value
Diameter | 6785km
Mass | 0.11 × Earth
Aerostationary orbit altitude | 17000km
Length of day | 24 hrs 37 mins
Length of year | 687 Earth days
Minimum distance from Sun | 205 million km
Maximum distance from Sun | 249 million km
Surface temperature | 174K to 308K
Gravity | 1 / 3 of Earth
Atmospheric pressure | 1 / 100 of Earth
Table 1. Martian Statistical Coefficients. [1]
Lower than Earth GEO
‘sol’
±20% light intensity
589W/m2 orbital power density (average)

## Slide 5: Mars Environment
Chart: 
The atmospheric composition (by volume) of Mars and Earth are shown [1] :
*Water vapor concentration on Earth ranges from 0.004% to 4%.
Chart: Atmospheric Composition of Mars
| CO2: 95.32% | N2: 2.70% | Ar: 1.6% | Oxygen: 0.13% | H20: 0.03% | Minor: 0.22%
Sales | 0.9532 | 0.027 | 0.016 | 0.0013 | 0.0003 | 0.0022
Chart: Atmospheric Composition of Earth*
| N2: 78% | Oxygen: 21% | Ar: 0.93% | CO2: 0.03%
Sales | 0.78 | 0.21 | 0.0093 | 0.0003
*Mars water vapor concentration is 1/1000 of Earth’s.
Notes: Highlight CO2

## Slide 6: Martian Dust Storms
One of the most remarkable features of Mars.
Local dust storm: frequent, last for few days, modest change of τ (optical depth).
( and are the surface light intensity in a vertical path with and without a dust cloud, respectively.)
Global dust storm: Once in several years, last for months, large change of τ.
Dust can be lifted to 60km high and could cause light attenuation of 0.35.
Figure 1. Global dust storm observed by Opportunity rover [2].
τ = 0.94
2.9
4.1
3.8
4.7
Notes: Tau is optical depth on a scale of 1 to 5
Observed by opportunity over a period of 30 sols

## Slide 7: Traditional Surface Power Systems By COMPASS team at John H Glenn Research Center
Surface Solar System
Equipped with 35% efficiency PV arrays.
Assume 120-day global dust storm with τ raised to 5.
12 hour daytime.
Panels periodically articulate +/- 45º to remove dust.
NASA/DOE Fission-Powered System
Equipped with radiation shield.
Reduce radiation to less than 3mR/hr within 500m.
Figure 2. Proposed Solar Array System. [2]
Figure 3. Proposed Fission System. [2]
Notes: Transition ISRU

## Slide 8: Traditional Surface Power Systems
ISRU System:
In-situ Resource Utilization (ISRU) converts CO2 to liquid oxygen (‘LOX’).
Performance measured by ISRU rate.
Mission Categories [2]:
Uncrewed mission:
10.8kg/sol LOX generation
Crewed mission:
44kg/sol LOX generation
5 crews living on Mars for 500 days
7kW continuous power
35kW continuous power
14.829kW keep-alive power
Notes: Keep alive power includes LOX production

## Slide 9: Traditional Surface Power Systems
 | Surface Solar System | Fission-Powered System
Working condition | Assume continuous | 
Power | 16kW daytime (8kW average) | 7kW, continuous
LOX production rate | 10.8kg/sol | 10.8kg/sol
Power system mass | 2425kg | 2751kg
Solar array | 7.5m diameter, four panels | none
Cost | 328 million dollars | 428.3 million dollars
Table 2. System comparison in uncrewed mission. [2]
Notes: Assume continuous
Talk about radiation shield
Talk about 8kW

## Slide 10: Traditional Surface Power Systems
 | Surface Solar System | Fission-Powered System
Working condition | Assume continuous | 
Power | 35kW (10kW during dust storms) | 35kW, continuous
LOX production rate | 44kg/sol | 44kg/sol
Power system mass | 11713kg | 9154kg
Solar array | 12m diameter, four systems | none
Cost | 455.8 million dollars | To be determined
Table 3. System comparison in crewed mission. [2]

## Slide 11: Mars SSP System Architecture
Power satellite is located in aerostationary orbit (17000km, 589W/m2).
Short eclipse: 1.28hr shadow (5% in one sol). (Ignore the shadow from ‘Phobos’)
Designed for crewed mission (35kW continuous power).
Use microwave to transmit power.
WPT Attenuation:
Free space, gaseous, dust

## Slide 12: WPT: Free Space Attenuation
Friis’ transmission equation:
Pt, Pr: Transmitted and received power; At, Ar: Antenna and rectenna aperture size;
λ: Microwave wavelength; D: Average distance between the antenna and rectenna.
Far-field constraint:
d: The antenna’s largest dimension.

## Slide 13: WPT: Atmospheric power loss
Gaseous attenuation
Permanent electric or magnetic moment could interact with microwave easily, such as in O2 and H2O.
Martian dominant gas CO2 does not have such moment.
The amount of O2 and H2O is very low on Mars.
Consider 10km height of the atmosphere, the gaseous attenuation is around 0.001 to 0.01dB, which is negligible.
Earth
Mars
Figure 4: Comparing gaseous attenuation for a horizontal path. [1]
Attenuation (dB/km) for a Horizontal Path
Frequency (GHz)
103
102
101
100
10-1
10-2
10-3
10-4
10-5
10-6
10-7

## Slide 14: Atmospheric power loss
Dust attenuation
Absorption and Scattering
Rayleigh scattering model
Permittivity: ε’ = 2.5 and ε’’ = 0.06 (at 35GHz) ε’ = 4.56 and ε’’ = 0.251 (at 2.45GHz)
Dust size distribution
r: radius of dust particles, distributed between 1 to 10μm.
at 35GHz ;
at 2.45GHz
Assume 4 μm average dust size, during global dust storm:
Sensitive to particle size

## Slide 15: System Coefficients
Solar array mass density* : 5kg/m2
Antenna mass density: 4kg/m2
Process | 2.45GHz case | 35GHz case
Orbiter PV arrays | 35% | 35%
Orbiter DC-to-RF conversion ηt | 85% | 75%
Rectenna elements efficiency ηr | 91% | 73%
Table 4. Energy Conversion Efficiency. [3,4]
* Data from 120V Orbital ATK UltraFlexTM arrays

## Slide 16: System coefficients
Mars orbit light intensity is 0.589kW/m2. PV arrays have 35% conversion efficiency.
The goal is to achieve a 35kW electric power.
(at 2.45GHz)
(at 35GHz)
Also, free space attenuation is in positive correlation with .

## Slide 17: System coefficients
(at 2.45GHz)
(at 35GHz)
Goal: Achieve minimum system mass and landed mass
System mass:
Landed mass:

## Slide 18: System Characteristics
Parameter | 2.45GHz | 35GHz
Size of orbital PV arrays | 158490m2 | 29203m2
Antenna aperture diameter | 500m | 215m
Rectenna aperture diameter | 200m | 90m
Distance | 17000km | 17000km
Received power | 35kW | 35kW
Landed mass | 126tons | 25tons
System mass | 1710tons | 317 tons
Table 5. Martian SSP system characteristics.

## Slide 19: Thoughts
Although Martian SSP system could weigh as much as several hundreds of tons. But one has to consider:
Based on the development of propulsion techniques, transporting large mass hardware to Mars will become practical.
A continuous, stable and low risk power can be generated using achievable technologies.
It has over 20-year lifetime. Once deployed, it can be applied for different missions, due to the flexibility of the power beaming.

## Slide 20: Propulsion system in the future
SpaceX interplanetary mission

## Slide 21: Thoughts
Although Martian SSP system could weigh as much as several hundreds of tons. But one has to consider:
Based on the development of propulsion techniques, transporting large mass hardware to Mars will become practical.
A continuous, stable and low risk power can be generated using achievable technologies.
It has over 20-year lifetime. Once deployed, it can be applied for different missions, due to the flexibility of the power beaming.

## Slide 22
Thank you!

## Slide 23: References
[1] Ho, Christian, Nasser Golshan, and Arvydas Kliore. "Radio wave propagation
handbook for communication on and around Mars." (2002).
[2] Rucker, Michelle A., et al. "Solar Versus Fission Surface Power for Mars." (2016).
[3] Cougnet, Claude, et al. "Solar power satellites for space applications." Journal of the British Interplanetary Society 59 (2006): 290-296.
[4] Jaffe, Paul, and McSpadden, James. "Energy conversion and transmission modules for space solar power." Proceedings of the IEEE 101.6 (2013): 1424-1437.